## Slide 1
Primer on Radiosonde
Tracking and Chasing
Presented to SCARS September 16, 2023

## Slide 2: Topics
What is a radiosonde?
Why would a ham be interested in them?
What is minimum I need to track?
What Info can I get while tracking?
What do I need to chase/recover?
What can I do with a recovered radiosonde?

## Slide 3: What is a Radiosonde?
High Altitude Balloon (HAB) with Sensor package attached
Sensors include GPS, temp, humidity, sometimes pressure
Routine launches at 0z & 12z daily from NWC on OU campus
Transmits Horus (4FSK) on 404.2MHz typically (400-406MHZ)
Balloon typically bursts ~115k ft, then parachute deploys
Flight lasts 2 to 3 ½ hours; Landing point varies dramatically
Landing points are predicted ahead of time, but are approximate
NWS suggests you recycle or dispose properly

## Slide 4: Radiosonde Balloon House

## Slide 5: Radiosonde Balloon Popped

## Slide 6: Common RadioSonde (RS41-NG)

## Slide 7: RadioSonde (RS41-NG) Internal

## Slide 8: Radiosonde Decode with SDR#

## Slide 9: Why would a Ham be Interested?
Possible Gateway into High Altitude or Pico Ballooning
Opportunity to practice for a fox hunt
Learn about how these data feed into weather prediction
Help kids/grandkids with possible school (STEM) projects
If retrieved:
  Can reprogram for ham frequencies, relaunch!
  Use as a GPS tracker, mini weather station, or “Fox”
… and ...

## Slide 10
FREE*
* Fuel and ER Charges Not Included :)
… it’s...

## Slide 11: Why would a Ham be Interested?
What do we get for FREE?
  Launch ready package containing:
  CPU: 32bit STM32F100C8 MCU
    24 MHz, 64kB flash
  GPS: UBLOX UBX-6010
  TX: SiLabs SI4032, max power ~60mw, Tuned to 70cm
  External I2C bus and UART serial port
  Powered by 2 AA batteries

## Slide 12: What is Minimum I Need to Track?
PC or smart device (phone, tablet) with a browser
Go to http://sondehub.org and scroll/zoom to our area
Click on ‘sonde of interest
Details of that ‘sonde appear in column on left
Examples in following slides

## Slide 13: What Info can I get while tracking?
If during launch (up to 2-3 hours after 6am or 6pm), can see
  Location of radiosonde as a balloon icon or parachute icon
  recent track and future (predicted) track
  Target icon (predicted landing site is updated periodically)
  Optionally display Skewed-T plot and other data charts
  List of other currently active radiosondes
  Location of chase cars (if they chose to be visible)
Otherwise, can see historical data from past launches

## Slide 14: Sondehub 7 Day Prediction

## Slide 15: Regional sondehub Live Map

## Slide 16: Example of local radiosonde track

## Slide 17: Example of Available Data

## Slide 18: More Data Examples

## Slide 19: More Data Examples

## Slide 20: “Non-Routine” launch from Sulpher

## Slide 21: What’s Needed to Track/Chase
We’ll focus on 2 options now
  RaspberryPi (RPi) based system
  LilyGo T-Beam STM32 development board

## Slide 22: What’s Needed to Track/Chase (RPi)
RaspberryPi 3 or 4 (Mouser: $55-$75)
Rtl-sdr (v3 w/.5ppm tcxo) USB w/ sma connector (Amazon: $35)
GPS dongle w/USB (Amazon: GlobalSat BU-353-S4, $35)
HDMI monitor (probably already have, get 12v for mobile)
Typical ham antenna for 70cm (probably already have)
Adapter cable between sma and pl259
If mobile, add appropriate battery/converter

## Slide 23: What’s Needed to Track/Chase (RPi)
For RPi Software
  Load/configure github.com/projecthorus/radiosonde_auto_rx
  Load/configure github.com/projecthorus/chasemapper
  Start web browser
  New tab for https://sondehub.org
  New tab for http://localhost:5000 to see ‘sonde from sdr dongle
  New tab for http://localhost:5001 for both ‘sonde and your gps

## Slide 24: Retrieval with Rpi-Based Tracker

## Slide 25: What’s needed to Track/Chase (T-Beam)
LilyGo T-Beam LoRa V1.1 ESP32 433MHz Dev Board, includes UHF receiver, WiFi, GPS, small display (Amazon $35)
18650 Lithium Battery or 5v phone recharger
Your phone/tablet/PC
Firmware from github.com/dl9rdz/rdz_ttgo_sonde
Install firmware into T-Beam
HT 70cm ham antenna

## Slide 26: ESP32 T-Beam

## Slide 27: Comparison: RPi and T-Beam
RPi based
  Some linux knowledge useful
  May have most of the pieces already
  Scans for strongest signal
  Maps on HDMI or phone
  Good for Base or Mobile
T-Beam based
  Easy to install firmware
  Easy to use, Few pieces
  Must predefine freqs
  Use phone/tablet for maps
  Send landing pt to phone or tablet and track there
  Great for chasing

## Slide 28: What’s Needed to Track (Other Options)
Windows 7 or 10 PC or Laptop
  Install Application Called RS41Tracker
  Install Zadig Windows driver for RTL-SDR
  Use RTL-SDR and GPS Dongles described previously
  Untested by me
Lilygo ESP32 LoRa Dev board w/o GPS (Amazon, $30)
  Similar to full ESP32, but can’t track your location

## Slide 29: What Can I Do with Recovered ‘Sonde?
1) Recycle with APRS protocol on Ham 70cm frequency
  Reflash f/w to HAM UHF frequency
    Need $15 ST-Link V2 interface (Amazon)
  Add Bosch BME280 sensor for Temp/HumidityPressure
  Add your callsign to config file
  Attach to new balloon
  Relaunch
  Track with Ham radios that supports APRS (on UHF)

## Slide 30: Reprogrammed for APRS on UHF

## Slide 31: What Can I Do with Recovered ‘Sonde?
2) Recycle with Horus protocol on Ham 70cm frequency
  Obtain registration from Horus group
  Attach ESP32 to insert HAM UHF frequency on power up
  Insert your callsign into firmware
  Attach to new balloon
  Relaunch
  Track on http://amateur.sondehub.org

## Slide 32: Amateur.sondehub.org (7 days)

## Slide 33: What Can I Do with Recovered ‘Sonde?
3) Use as a hardwired GPS tracker
  Attach to serial port of ‘sonde (9600 baud)
  Sends out NMEA formated location data
4) Use as a mini Weather Station
  Sends out temperature and humidity on serial port
5) Use as a Fox for Foxhunt
  Program it to send out club callsign in CW

## Slide 34: Live Demo by Rick
Live Demos
Correct Bob’s disinformation
Comments on ‘sonde recovery challenges

## Slide 35: Next Steps?
How Do I get started?
  Elmer Night is a good place for followup
How do we launch ‘sondes or other beacons?
  Some balloon history already here in club?
  See if enough interest to send balloons up?
Possibly install tracking station on OU campus?
Possibly team up with elementary/middle schools for STEM?
Do a foxhunt?

## Slide 36: Possible Weather/Balloon/Radio Template
See HABGab 2023 project from New England SCI-TECH at http://nescitech.org
  From a single 2000g weather balloon:
  Crossband UHF/VHF repeater that lasted 2-3 hours
  Auto-rotation copter released at 80k ft w/ lightAPRS tracker
  Glider released at 80k ft w/ tracker, APRS on 144.390
  Live 2 camera video feed at 1.2GHz
  Main payload with repurposed RS41 ‘sonde on 432.501MHz

## Slide 37: Primer on Radiosonde Chasing
Questions/Comments?